## Slide 1: Vlans
Networks

## Slide 2: Vlans
VIRTUAL LANs : local area network configured by software, not by physical wiring.
VLANs define broadcast domains in a Layer 2 network. A broadcast domain is the set of all devices that will receive broadcast frames originating from any device within the set.

## Slide 3: Configuration
Configuration : How are the stations grouped into different VLANs ?
Stations are configured in one of three ways : manual, semiautomatic, and automatic .
Manually : via the command line interface (CLI) or web interface .
Automatically : with a standard protocol like GVRP (GARP VLAN Registration Protocol), which works in conjunction with 802.1Q.
automatically with a proprietary protocol like Cisco’s VTP (Virtual Trunking Protocol), which works in conjunction with Cisco’s proprietary ISL (Inter-Switch Link) trunking protocol.

## Slide 4: Parameters
You can set the following parameters when you create a VLAN in the management domain :
VLAN number
VLAN name
VLAN type
VLAN state (active or suspended)
Maximum transmission unit (MTU) for the VLAN
Security Association Identifier (SAID)
VLAN number to use when translating from one VLAN type to another

## Slide 5: Membership
What characteristic can be used to group stations in a VLAN?
Port Numbers .
MAC Addresses .
IP Addresses .
Multicast IP Addresses .
Combination .

## Slide 6: Trunk
A trunk is a communications line or link designed to carry multiple signals simultaneously to provide network access between two points. Trunks typically connect switching centers in a communications system. The signals can convey any type of communications data. A trunk can consist of multiple wires, cables or fiber optic strands bundled together to maximize the available bandwidth in a single physical cable, or it can consist of a single high-capacity link over which many signals are multiplexed.

## Slide 7: Advantages of Vlans
Cost and Time Reduction : VLANs can reduce the migration cost of stations going from one group to another. Physical reconfiguration takes time and is costly. Instead of physically moving one station to another segment or even to another switch, it is much easier and quicker to move it by using software.

## Slide 8: Advantages of Vlans
Creating Virtual Work Groups : VLANs can be used to create virtual work groups. For example, in a campus environment, professors working on the same project can send broadcast messages to one another without the necessity of belonging to the same department. This can reduce traffic if the multicasting capability of IP was previously used.

## Slide 9: Advantages of Vlans
Security : VLANs provide an extra measure of security. People belonging to the same group can send broadcast messages with the guaranteed assurance that users in other groups will not receive these messages.

## Slide 10: Disadvantage
VLANs also have some disadvantages and limitations as listed below :
High risk of virus issues because one infected system may spread a virus through the whole logical network
Equipment limitations in very large networks because additional routers might be needed to control the workload
More effective at controlling latency than a WAN, but less efficient than a LAN

## Slide 11: Questions
How does a VLAN save a company time and money ?
A VLAN saves time and money because reconfiguration is done through software . Physical reconfiguration is not necessary.

## Slide 12: Questions
How does a VLAN provide extra security for a network ?
Members of a VLAN can send broadcast messages with the assurance that users in other groups will not receive these messages.

## Slide 13: Questions
How does a VLAN reduce network traffic ?
A VLAN creates virtual workgroups. Each workgroup member can send broadcast messages to others in the workgroup. This eliminates the need for multicasting and all the overhead messages associated with it.

## Slide 14: Questions
What is the basis for membership in a VLAN ?
Stations can be grouped by port number, MAC address, IP address, or by a combination of these characteristics.

## Slide 15: Practice

## Slide 16: Practice

## Slide 17: Practice

## Slide 18: Practice

## Slide 19: Practice

## Slide 20: Practice

## Slide 21: Practice

## Slide 22: Practice

## Slide 23: Practice

## Slide 24: Practice

## Slide 25: Practice

## Slide 26: Practice

## Slide 27: Practice

## Slide 28: Practice

## Slide 29: Practice

## Slide 30: Done …
Msc. Mustafa Abbas A. Al-Khafaji
Atilim University
2018