## Slide 1
CIV 331
Highway Engineering
Course Instructor
Dr. Essam Dabbour, P. Eng.
Presentation 05

## Slide 2: DESIGN OF HORIZONTAL CURVES
2

## Slide 3: CONCEPTUAL APPROACH
3
The critical design feature of horizontal alignment is the horizontal curve that transitions the roadway between two straight (tangent) sections.
Vehicle cornering capability is thus a key concern in horizontal curve design.

## Slide 4: VEHICLE CORNERING ON HORIZONTAL CURVES
4
Rv = radius defined to the vehicle’s traveled path in ft (m),
 = angle of incline in degrees,
e = number of vertical ft (m) of rise per 100 ft (m) of horizontal distance,
W = weight of the vehicle in lb (N),
Wn = vehicle weight normal to the roadway surface in lb (N),
Wp = vehicle weight parallel to the roadway surface in lb (N),
Ff = side frictional force (in lb (N)),
Fc = centripetal force (lateral acceleration x mass, in lb (N)),
Fcp = centripetal force acting parallel to the roadway surface in lb (N), and
Fcn = centripetal force acting normal to the roadway surface in lb (N).

## Slide 5: VEHICLE CORNERING ON HORIZONTAL CURVES (Cont’d)
5
Some basic horizontal curve relationships can be derived by noting that: Wp + Ff = Fcp
From basic physics this equation can be written as [with Ff = fs(Wn + Fcn)]:
(where fs is the coefficient of side friction)
Dividing both sides of the previous equation by W cos  yields:

## Slide 6: VEHICLE CORNERING ON HORIZONTAL CURVES (Cont’d)
The term tan  is referred to as the superelevation of the curve and is denoted e (e = 100 tan ).
Being conservative and ignoring the normal component of centripetal force (fs tan ), and with e = 100 tan , the above equation can be rearranged as follows:
Selected value of e is critical because high rates of superelevation can cause vehicle steering problems on the horizontal curve, and in cold climates, ice on the roadway can reduce fs such that vehicles traveling less than the design speed on an excessively superelevated curve could slide inward off the curve by gravitational forces.

## Slide 7: VEHICLE CORNERING ON HORIZONTAL CURVES (Cont’d)
Selecting a superelevation, e, a design speed, V, and using maximum side friction, fs, a minimum radius is obtained.
The maximum side friction, fs, depends on the design speed (empirical values).
Design guides (e.g., AASHTO) provide tables for maximum side friction, fs, and curve radius for different values of design speeds and superelevation. (see pages 76-77).

## Slide 8: DESIGN VALUES FOR e, f AND R [AASHTO]

## Slide 9: SIMPLE CIRCULR HORIZONTAL CURVE
R = radius, usually measured to the centerline of the road, in ft (m),
 = central angle of the curve in degrees,
PC = point of curve (the beginning point of the horizontal curve),
PI = point of tangent intersection,
PT = point of tangent (the ending point of the horizontal curve),
T = tangent length in ft (m),
M = middle ordinate in ft (m),
E = external distance in ft (m), and
L = length of curve in ft (m).

## Slide 10: SIMPLE CIRCULR HORIZONTAL CURVE
Some other relationships:

## Slide 11: EXAMPLE 1
A horizontal curve is designed with 610-m radius. The curve has a tangent length of 120 m and the PI is at station (3+140). Determine the station of PT.
[see whiteboard or page 82]

## Slide 12: SSD ON HORIZONTAL CURVES
Sight distance restrictions on horizontal curves occur when obstructions (e.g., buildings, signs) are present as shown in the figure.
When such an obstruction exists, the stopping-sight distance is measured along the horizontal curve from the center of the traveled lane (the assumed location of the driver’s eyes).
for a specified stopping distance, some distance, Ms, must be visually cleared to provide the required stopping sight distance.
Equations for computing stopping-sight distance relationships for horizontal curves can be derived by first determining the central angle, s, for an arc equal to the required stopping-sight distance.

## Slide 13: EQUATIONS FOR SSD ON HORIZONTAL CURVES
®
Substituting into the general equation for the middle ordinate of a simple horizontal curve gives:
Solving the above equation for SSD gives:

## Slide 14: EXAMPLE 2
A horizontal curve on a two-lane highway is designed with a 610-m radius, 3.6-m lanes and 100-km/h design speed (required SSD = 185 m). Determine the distance that must be cleared from the inside edge of the inner lane to provide a sufficient stopping sight distance.
[see whiteboard]

## Slide 15: EXAMPLE 3
A horizontal curve on a 4-lane highway (two lanes in each direction with no median) has a superelevation of 6% and a central angle of 40 degrees. The PT of the curve is at station 9+830 and the PI is at 9+756. The road has 3.1 m lanes and 2.8 m shoulders on both sides with high retaining walls going up immediately next to the shoulders. You are required to calculate the following:
The highest possible design speed of this curve (rounded to the nearest 10 km/h).
The station of PC on that curve.
[see whiteboard or page 84]

## Slide 16: EXAMPLE 4
A very long horizontal curve on a level one-directional racetrack has 1750-meter centerline radius, two 4-meter lanes, and a 200 km/h design speed. Determine the closest distance from the inside edge of the track that spectators can park without impeding the necessary sight distance of the drivers. Assume that the sight distance is less than the length of the curve, a deceleration rate of 3.5 m/sec/sec, and a perception-reaction time of 2.5 seconds.
[see whiteboard]

## Slide 17: EXAMPLE 5
A given horizontal curve has two-lanes with lower-than-average coefficient of side friction (0.05) and no superelevation. The lane width is 4-meter. The curve has a radius of 500 meter and a design speed of 80 km/hr. As an engineer, you need to check the safety of this curve. How can you show this?
[see whiteboard]

## Slide 18: COMBINED VERTICAL & HORIZONTAL CURVES
18

## Slide 19: EXAMPLE 6
A two-lane highway with lane width 3.6 m has a posted speed limit of 80 km/h and on one section it has both horizontal and vertical curves as shown in the figure below. A recent daytime crash occurred where a driver was traveling eastbound and collided with a stationary roadway object. A lawsuit is alleging that the posted speed (80 km/h) is unsafe speed for the curves in question and was a major cause for the crash. Evaluate the roadway design.
[see whiteboard or page 86]

## Slide 20: EXAMPLE 7
A new highway is to be constructed over an existing highway. The two highways are level and should intersect at right angle with grade separation. The new highway will run east-west and the existing highway runs north-south at elevation 172 m. The proposed bridge structure for the new highway is such that the bridge girder thickness is 2 m (measured from the road surface to the bottom of the girder). A single-lane ramp is to be constructed to allow east-bound traffic to go southbound. With the design speed 70 km/h and superelevation 4%, and assuming the curve begins at station 1+219, you are required to determine the stations of PI and PT as well as the stations and elevations of all key points along the vertical alignment. Also, calculate the distance that must be cleared from the inside of the horizontal curve to ensure sufficient SSD.
[see whiteboard or page 87]

## Slide 21: CROSS SECTION ELEMENTS
21

## Slide 22: CROSS SECTION OF AN URBAN STREET (AASHTO)

## Slide 23: CITY BOULEVARD (USDM)

## Slide 24: CITY AVENUE (USDM)

## Slide 25: CITY STREET (USDM)

## Slide 26: URBAN STREET CLASSIFICATION (USDM)

## Slide 27: AASHTO vs. USDM CLASSIFICATION

## Slide 28: MUSHTARAK (SHARED) STREET – USDM

## Slide 29: LANE WIDTH
Range (3.00 m – 3.70 m).
Depends on different factors:
  Design vehicle;
  Type of highway (urban or rural);
  Design speed; and
  Traffic volume.
For rural local roadways it ranges from 3.00 m to 3.70 m.
For urban roadways and multilane rural roadways it ranges from 3.30 m to 3.70 m (narrower lanes are preferred for safety).
Lanes wider than 3.70 m don’t improve safety.
Lanes wider than 4.00 m may have negative impact on safety.

## Slide 30: CROSS SECTION OF A RURAL ROADWAY (AASHTO)

## Slide 31: SHOULDERS
Shoulders have many advantages, including:
  A recovery area for errant vehicles.
  A refuge for stopped or disabled vehicles.
  Stopping area for emergency and maintenance vehicles.
  Lateral support for roadway pavement.
  Improved sight distance.
  Improved highway capacity.
Shoulders are usually provided on rural roads and urban roads with design speeds higher than 80 km/h.

## Slide 32: PAVEMENT MATERIALS FOR SHOULDERS
Shoulders are either:
  Covered with gravel;
  Partially paved (with paved width 0.8 m); or
  Completely paved (paving colour and/or texture should contrast from paving material for the roadway).
For paved shoulders, in addition to the contrast of pavement material, it is also desirable to use rumble strips.
The typical dimensions of a rumble strip are 600mm x 50mm, and spaced at 200mm.

## Slide 33: FREEWAY MEDIANS