## Slide 1
CIV 331
Highway Engineering
Course Instructor
Dr. Essam Dabbour, P. Eng.
Presentation 02

## Slide 2: ROAD-VEHICLE PERFORMANCE
2
Roadway design is governed by two main factors:
  Vehicle capabilities
    acceleration/deceleration
    braking
    cornering
  Human capabilities
    perception/reaction times
    eyesight (range, height above roadway)
Performance of road vehicles forms the basis for roadway design guidelines such as:
  length of acceleration / deceleration lanes
  maximum grades
  stopping-sight distances / passing-sight distances
  timing of traffic signals

## Slide 3: TRACTIVE EFFORT AND RESISTANCE
3
These are the opposing forces that determine straight-line performance of road vehicles.
Tractive effort is simply the force available at the roadway surface to perform work (expressed in lbs [N]).
Resistance (expressed in lbs [N]) is defined as the force impeding vehicle motion.
Three major sources of vehicle resistance are:
  Aerodynamic
  Rolling (originates from the roadway surface-tire interface)
  Grade or gravitational

## Slide 4: TRACTIVE EFFORT AND RESISTANCE
4
Ff + Fr = ma + Ra + Rrlf + Rrlr + Rg
F = ma + Ra + Rrl + Rg

## Slide 5: AERODYNAMIC RESISTANCE
5
It can have significant impacts on vehicle performance, particularly at high speeds.
It can be determined using the following equation:
Where:
Ra = aerodynamic resistance in lb (N) ρ (rho) = air density in slugs/ft3 (kg/m3) CD = coefficient of drag (unitless) Af = frontal area of vehicle in ft2 (m2) V = vehicle speed in ft/s (m/s)

## Slide 6: AERODYNAMIC RESISTANCE (Cont’d)
6
Air density is a function of both elevation and temperature (see Table 2.1 in the textbook).
The drag coefficient is measured from empirical data, either from wind tunnel experiments or actual field tests (it has dropped from about 0.5 to mid 0.2’s for sedan type vehicles, but still in 0.4 – 0.5 range for SUVs and trucks).
2005 Honda Insight (CD = 0.25)
1967 Volkswagen Beetle (CD = 0.46)
2003 Hummer H2 (CD = 0.57)
2010 Toyota Prius (CD = 0.25)

## Slide 7: AERODYNAMIC RESISTANCE (Cont’d)
7
As power is the product of force and speed, the power needed to overcome aerodynamic resistance can be determined using the following equation:
The force required to overcome aerodynamic resistance increases with the square of the speed while the corresponding power increases with the cube of the speed (double the speed requires 4 times the force and 8 times the power).

## Slide 8: ROLLING RESISTANCE
8
Refers to the resistance generated from the interaction between the tires and the roadway surface:
  Primary source (about 90%) of this resistance is the deformation of the tire as it passes over the roadway surface.
  Tire penetration/roadway surface compression (about 4%)
  Tire slippage and air circulation around tire & wheel (about 6%)
Factors affecting rolling resistance (Rrl ):
  Rigidity of tire and roadway surface
  Tire inflation pressure and temperature
  Vehicle speed

## Slide 9: ROLLING RESISTANCE
9
Rolling resistance is calculated using the following approximated equation:
Since grades are often small, the equation is further simplified by assuming that cos g = 1 (giving a slightly more conservative estimate), yielding:
Coefficient of rolling resistance (frl) for road vehicles operating on paved surfaces is approximated as:
with V in m/s

## Slide 10: GRADE RESISTANCE
10
The grade resistance is the component of the vehicle weight acting parallel to the roadway surface.
As highway grades are usually small:

## Slide 11: EXAMPLE 1
11
A 8.9 kN car has a drag coefficient of 0.40, frontal area 2.0 m2 and an available tractive effort of 1.135 kN. Determine the maximum grade that the car can ascend at an elevation 1500 m (ρ = 1.0567 kg/m3) on a paved surface while maintaining a maximum speed of 110 km/h.
[see whiteboard and pages 15 - 16]

## Slide 12: EXAMPLE 2
12
If the car in the previous example was travelling at a speed of 90 km/h on 1% down grade, determine the maximum rate of acceleration it can attain.
[see whiteboard]

## Slide 13: MAXIMUM TRACTIVE EFFORT
13

## Slide 14: MAXIMUM TRACTIVE EFFORT (Cont’d)
14
No matter how much force a vehicle’s engine produces at the roadway surface, there is a point beyond which additional force will not accelerate the vehicle further but rather it will just result in the spinning of tires.
To determine that maximum tractive effort, the normal load on the rear axle (Wr) is determined by summing the moments about point A:
Since the grade is usually small then cosθ = 1 and the above equations becomes:

## Slide 15: MAXIMUM TRACTIVE EFFORT (Cont’d)
15
From the basics of physics, the maximum tractive force is the product of the normal force (Wr) multiplied by the coefficient of road adhesion (µ); and therefore, the maximum tractive force for a rear-wheel-drive vehicle is:
Similarly, by summing moments about point B, it can be shown that for a front-wheel-drive vehicle:

## Slide 16: TYPICAL VALUES OF COEFFICIENT OF ROAD ADHESION
16
Pavement | Coefficient of Road Adhesion | 
 | Maximum | Slide
Good, dry | 1.00 | 0.80
Good, wet | 0.90 | 0.60
Poor, dry | 0.80 | 0.55
Poor, wet | 0.60 | 0.30
Packed snow or ice | 0.25 | 0.10

## Slide 17: EXAMPLE 3
17
An 11.0-kN car is designed with 3.05 m wheelbase. The center of gravity is located 550 mm above the pavement and 1.00 m behind the front axle. If the coefficient of road adhesion is 0.6, what is the maximum tractive effort that can be developed if the car is (a) front-wheel-drive and (b) rear-wheel-drive?
[see whiteboard and page 18]

## Slide 18: PRINCIPLES OF BRAKING
18
For roadway design and traffic analysis, vehicle braking characteristics are the most important aspect of vehicle performance.
Braking performance is a key factor to the determination of:
  stopping-sight distance, which is one of the foundations of roadway design
  the length of the yellow interval for traffic signals

## Slide 19: PRINCIPLES OF BRAKING
19

## Slide 20: PRINCIPLES OF BRAKING
20
Taking moments about the front and rear axles, and assuming cos g = 1 for small roadway grades, the normal loads on the front and rear axles are given by the following equations:
Also, from summing forces along the vehicle’s longitudinal axis gives:
where: Fb = Fbf + Fbr

## Slide 21: PRINCIPLES OF BRAKING
21
Substituting the equations together yields the following equations :
The maximum vehicle braking force (Fb max) is equal to the coefficient of road adhesion times the weights normal to the roadway surface:
 = coefficient of road adhesion
(front braking force)
(rear braking force)

## Slide 22: PRINCIPLES OF BRAKING
22
Substituting the equations together again yields the following equations :
To develop maximum braking forces, the tires should be at the point of impending slide.
If the tires begin to slide (i.e., the brakes lock), a significant reduction in road adhesion will result.

## Slide 23: EXAMPLE 4
23
Calculate the minimum coefficient of road adhesion to ensure that a car will not slide given that the car is front-wheel driven with the braking force produced at tire-pavement contact point is 2.1 kN, the car speed is 90 km/h, its weight is 8.7 kN and the length of its wheel base is 1.95 m with its center of gravity is at distance 0.90 m from the front axle and at height 0.55 m above roadway surface.
[see whiteboard]