## Slide 1
CIV 331
Highway Engineering
Course Instructor
Dr. Essam Dabbour, P. Eng.
Presentation 03

## Slide 2: PRACTICAL STOPPING SIGHT DISTANCE
2
SSD on vertical curves

## Slide 3: PRACTICAL STOPPING SIGHT DISTANCE
3
SSD on horizontal curves

## Slide 4: PRACTICAL STOPPING SIGHT DISTANCE
4
From the basic physics for rectilinear motion:
where:
V2 = final vehicle speed [m/s];
V1 = initial vehicle speed [m/s];
a = acceleration (or deceleration) [m/s2]; and
d = acceleration (or deceleration) distance [m].

## Slide 5
Re-arranging the equation for deceleration:
If the vehicle comes to a complete stop, the equation becomes:
PRACTICAL STOPPING SIGHT DISTANCE

## Slide 6
If the vehicle is on a grade, the equation becomes:
Substituting for the gravitational constant (g), the equation becomes:
Where (d) is the distance [m], (V) is the speed [km/h], (a) is deceleration rate and (G) is the percentage of grade divided by 100.
PRACTICAL STOPPING SIGHT DISTANCE

## Slide 7
Studies show that most drivers decelerate at the following rate:
In providing sufficient sight distance for a driver to stop safely, it is necessary to consider the distance traveled during the perception/reaction time required for the driver to perceive and react to the need to stop. It is calculated as:
where (V1) is the initial speed [m/s] and (tr) is the time required to perceive and react to the need to stop [approximately 2.5 seconds]
PRACTICAL STOPPING SIGHT DISTANCE

## Slide 8
The final equation for the stopping sight distance becomes:
General Notes:
There are tables in design guides that give stopping sight distance (SSD) based on the above equation for different speeds and grades.
In determining SSD for highway design, the driver’s eye height above the road surface is assumed to be 1.05 m [AASHTO; TAC], and the height of the object to be (0.00 m– 0.38 m) [TAC] or (0.60 m) [AASHTO].
Trucks need lesser rate of deceleration and therefore longer SSD. However, a truck driver is able to see further than a passenger car driver because of the seat’s higher position.
PRACTICAL STOPPING SIGHT DISTANCE

## Slide 9: EXAMPLE 1
9
Two drivers traveling on 2.5% downgrade road that has a speed limit 90 km/h. Both drivers have a perception-reaction time of 2.5 seconds. If one of the two drivers is obeying the speed limit and the other driver is traveling illegally at 120 km/h, calculate the following:
  The distance that each of the drivers need to perceive/react to the need to stop.
  The total stopping distance needed for every driver.
[see whiteboard]

## Slide 10: STOPPING SIGHT DISTANCE [AASHTO]

## Slide 11: PASSING SIGHT DISTANCE
Passing sight distance (PSD) is the distance required for a vehicle to overtake a slower moving vehicle safely on a two-lane highway.
While the SSD is required to be provided continuously throughout all types of highways, PSD is required to be provided only on two-lane highways where possible.
Lane marking and signage are used to inform the drivers whether passing is allowed or not.

## Slide 12: PASSING SIGHT DISTANCE

## Slide 13: PASSING SIGHT DISTANCE
  d1: Distance during perception/reaction time and during the initial acceleration of the passing vehicle;
  d2: Distance traveled while the passing vehicle occupies the left lane;
  d3: Distance between the passing vehicle at the end of its maneuver and the opposing vehicle; and
  d4: Distance traversed by the opposing vehicle for 2/3 of the time the passing vehicle occupies the left lane.

## Slide 14: PASSING SIGHT DISTANCE [AASHTO]

## Slide 15: DECISION SIGHT DISTANCE
Decision sight distance (DSD) is required at complex locations to enable drivers to maneuver their vehicles safely without stopping or substantially reducing their speeds.
It is the distance traversed during the time required for the driver to detect a complex situation, recognize it, decide on proper maneuver and execute the required action.
Examples for locations where DSD is required:
  Complex interchanges.
  Toll plazas.
  Lane drops.
  …

## Slide 16: DECISION SIGHT DISTANCE

## Slide 17: DECISION SIGHT DISTANCE

## Slide 18: DECISION SIGHT DISTANCE

## Slide 19: DECISION SIGHT DISTANCE [AASHTO]